## Slide 1: On Controllability of Leader-Follower Dynamics over a Directed Graph
Jayakumar Subramanian, Aditya Mahajan and Aditya A. Paranjape
57th IEEE Conference on Decision and Control, Miami Beach, FL, USA, December 17-19, 2018

## Slide 2: Networked systems are everywhere…
Image credit: BRIDGE8
Image credit: Networkworld
Image credit: WhaTech
Image credit: TheNextWeb.com
Can we determine controllability from structure alone?
Notes: Networked systems are everywhere around us. These are multi-agent systems on graphs. There are several examples of such systems like mobile robotics, sensor networks, distributed energy systems, social networks etc. A common framework to analyze these systems is to model them as a graphs with nodes as agents, edges as dynamical couplings and more often than not dynamics represented in terms of the graph Lalplacian. Most of the literature considers undirected graphs, but there are models in which the dynamical coupling is best modelled by directed graphs. In this work we focus on such directed graphs. The question we shall attempt to answer in our work is this: Can we determine controllability of such networks just by looking at the graph structure and not the specific edge-weights?

## Slide 3: Dynamics
1
7
8
3
2
5
4
6
Leader-follower system
Leaders
Followers
In-Laplacian
Dynamics
Notes: In this work we consider a leader-follower system as shown in this graph. Each node is an agent and each directed edge represents a dynamical connection between agents. The strengths of these connection is determined by the edge-weights, which are non-zero real numbers. The agents are partitioned into two sets – leaders and followers. The nodes shown in orange are the leaders which can be directly influenced by control inputs. The blue nodes are followers and can only be indirectly influenced through system dynamics.

## Slide 4: 1st motivating example
2
3
4
8
6
7
1
5
9
Notes: Throughout this talk I will consider two motivating examples. The first one is the graph shown here. Which are the nodes in this graph that can be considered as leaders, that is, the nodes that require external control input so that the system is controllable? Is this controllability dependent on the edge-weights? These questions will be addressed in the remainder of my talk.

## Slide 5: 2nd motivating example
2
3
4
8
6
7
1
5
9
2
3
4
8
6
7
1
5
9
?
?
Notes: For the second example, we consider two graphs. We ask the following question here. If we know which leaders to pick to make each of these graphs controllable, how do we connect these two graphs and ensure that the resulting system is also controllable? That is, how do we pick which nodes from the first graph to connect to which nodes from the second graph and which nodes to pick as leaders such that the cascade of these two graphs is controllable? These questions will also be answered in the rest of my talk.

## Slide 6: System controllability
Complicated leader-follower network with unknown weights
Is this system controllable?
Example 1
1
2
3
Graph structurally controllable
Example 2
1
2
Strong graph structurally controllable
3
Graph structural controllability
A graph structure is graph structurally controllable if there exists a weight function such that the system is controllable.
A graph structure is strong graph structurally controllable if for every weight function the system is controllable.
Strong graph structural controllability
Can we decide this based only on the structure?
Notes: Suppose we have a complicated network of a leader-follower system and the weights are unknown. Can we say if the system is controllable? Let us look at 2 examples. The first example is controllable for any choice of weights other than w_12 = w_13. We call such a system as graph structurally controllable. By graph structurally controllable

## Slide 7: Literature overview
  Structural controllability: [Lin, 1974]
  Strong structural controllability: [Mayeda & Yamana, 1979]
  Various necessary and sufficient conditions for controllability of leader-follower dynamics over undirected graphs: [(Tanner, 2004), (Rahmani et al., 2009), (Ji et al., 2009), (Ji et al., 2012), (Parlangeli & Notarstefano, 2012), (Notarstefano & Parlangeli, 2013), (Aguilar & Gharesifard, 2015) and others].
  Necessary conditions for controllability of leader-follower dynamics over directed graphs: [Aguilar and Gharesifard, 2016]
  Zero forcing: [Monshizadeh et al., 2014]
Structural controllability
Graph structural controllability
Strong graph structural controllability
Strong structural controllability
Notes: Analysis of controllability of graphs based on structure alone can be found in the work of Lin and strong controllability can be found in the work of Mayeda and Yamada. As I explained earlier, these concepts are defined for generic graphs and not for leader-follower systems. These concepts are different from those of structural and strong structural controllability for graphs defined in literature. Structural controllability and strong structural controllability are defined for any linear system. The only condition when considering alternate weight functions is that the sparsity pattern of the system dynamics matrix A and control matrix B are preserved. In our case, i.e., in leader-follower dynamics, the system dynamics matrix is the in-Laplacian of the graph. Hence, when we consider alternate weight functions, we need to ensure that the resulting system also has a system dynamics matrix that is the in-Laplacian with the new weight function. This is equivalent to having the condition that the new system dynamics matrix has the same sparsity structure as the old one with the added condition that all its rows sum to zero, just as the old one. Thus, we can see that graph structural controllability is a stronger property than structural controllability and strong graph structural controllability is a weaker property than strong structural controllability.
For leader-follower systems over undirected graphs, various necessary and sufficient conditions have been specified in Tanner, Rahmani et al. Ji eta al, Parlangeli and Notarstefano and Aguilar & Gharesfard. Aguilar & Gharesfard also have a paper on necessary conditions for controllability of leader-follower dynamics over directed graphs using almost equitable partitions. Finally, there is a closely related concept of zero-forcing for directed graphs by Monshizadeh et al. which assumes a slightly different model than leader follower dynamics.

## Slide 8: Graph structural controllability
Theorem 1
The system is graph structurally controllable if and only if for any weight function and any , there exists a weight function satisfying such that the system is controllable.
Theorem 2
A leader-follower system is graph structurally controllable if and only if
every node is accessible from some leader node.
Notes: We shall now look at two theorems on graph structural controllability. The first theorem formally defines the condition for a system to be graph structurally controllable. The second theorem gives a structural condition for s system to be graph structural controllability. We can show that accessibility from a leader node is necessary and sufficient for a system to be graph structurally controllable. Thus, GSC is trivially satisfied in all systems of interest

## Slide 9: Example for Theorem 2
1
7
8
3
2
5
4
6
Graph structurally controllable
1
7
8
3
2
5
4
6
Not
graph structurally controllable
Not accessible from 1 or 2
Notes: We now look at two examples to illustrate Theorem 2. In each of these examples let nodes 1 and 2 be the leaders. In the first example all nodes can be accessed from nodes 1 or 2. Hence this system is graph structurally controllable. In the second example, the only difference is the the edge from 5 to 4 is now reversed into an edge from 4 to 5. This makes node 4 inaccessible from either of nodes 1 or 2. Thus, this system is not graph structurally controllable.

## Slide 10: 1st motivating example
2
3
4
8
6
7
1
5
9
Graph structurally controllable
Notes: We now return to the question of controllability of our first motivating example. In this graph, we find that for any choice of leader, all nodes are accessible from the leader. Hence, this system is graph structurally controllable for any choice of leader.

## Slide 11: Strong graph structural controllability
Theorem 3
In a leader-follower system with a single leader, suppose there exists a permutation such that:
is the leader node
is a Hamiltonian path
For any such that , the graph does not have an edge from node to node .
The system is strong graph structurally controllable.
For any weight function , the eigenvalues of the controllability matrix of this system are:
,
for
Notes: We now come to the main theorem in this paper. This theorem gives a sufficient condition for strong graph structural controllability. Suppose in a leader follower system, we can index the nodes in such a way that i_1 is the leader, i_1 to i_n is a Hamiltonian path and there are no back edges in terms of this ordering, we then have the the system is strong graph structurally controllable and the eigenvalues of the associated controllability matrix can be expressed as the cumulative products of the edge-weights of this Hamiltonian path starting from a value of 1. Knowing the eigenvalues allows us to determine the condition number of the controllability matrix. A condition number close to unity implies that the minimum energy is almost equal for all (eigen) directions. Thus, in addition to controllability, we also get information about how far the system is from being uncontrollable.

## Slide 12: 1st motivating example
2
3
4
8
6
7
1
5
9
Notes: Again coming back to our first motivating example, we now pick leaders for which we can say that this system is string graph structurally controllable. There are two such leaders in this graph. The first one is node 6. From node 6 we can see that there exists a Hamiltonian path as shown in the graph and there are no additional forward edges. The next leader is node 8. For this node too, there exists a Hamiltonian path with no additional forward edges. Thus, for these two choices of leaders, we can conclude that the system is strong graph structurally controllable.

## Slide 13: A necessary condition
Theorem 4
Suppose in a leader-follower system, there exist nodes such that:
nodes are not leaders;
;
;
.
Then, the system is not controllable.
i
k
j
E.g. 1
i
k
j
E.g. 2
Notes: We now look at a necessary condition for strong graph structural controllability by looking at triangular sub-structures. To illustrate the conditions of this theorem, we consider two examples. Suppose we have three nodes i, j and k in a leader-follower system which satisfy four conditions, i.e, nodes j and k are not leaders, either only i is the in-neighbour of j as in example 1 or or both i and k are in-neighbours of j as in example 2. However both i and j are in-neighbours of k. The final condition is that either the weights on the i-j and i-k edges are equal or the sum of binary weight products given here is 0. Then, we can conclude that this triangular system is not controllable.

## Slide 14: A necessary condition - corollary
Corollary to Theorem 4
A system with a triangular sub-graph satisfying conditions 1,2, and 3 of Theorem 4 is not strong graph structurally controllable.
i
k
j
Example
g
b
a
c
d
f
e
Notes: A corollary to Theorem 4 that extends the results to larger graphs with unknown weights is as follows. Let us consider a system which has a triangular sub-graph satisfying conditions 1,2, and 3 of Theorem 4. Then we can say that this system is not strong graph structurally controllable. As an example, consider the graph shown here. Here the nodes i, j and k satisfy the structural conditions of Theorem 4. Hence, we can conclude that this system is not strong graph structurally controllable.

## Slide 15: Controllability of cascades
1
2
Example of a cascade
3
4
5
Cascade
1
2
3
4
5
Theorem 5
Consider two systems where:
satisfies conditions of Theorem 3;
is controllable;.
Then, the cascaded system formed by connecting the terminal node of
to the leader of with any weight (and making the leader of a follower) is controllable.
Notes: The last part of our work deals with controllability of cascades. Suppose we have two systems G1, M1, w1 and G2, M2, w2 as shown in the example figures. Note that both these systems in the example are strong graph structurally controllable. A cascade formed by these by connecting node 1 to node 3 is not strong graph structurally controllable. Thus, given two strong graph structurally controllable systems, it is not necessary that a cascade of these two systems is also strong graph structurally controllable. So we ask this question – if we know something about the controllability of two graphs, what can we say about the controllability of a cascade formed by these two? This leads us to our final theorem which states sufficient conditions for controllability of cascades. Suppose G1 is strong graph structurally controllable and the system G2,M2,w2 is controllable. Then, we can prove that the cascaded system formed by connecting the last node of G1 to the leader of G2 with any weight and making it a follower is controllable.

## Slide 16: 2nd motivating example
2
3
4
8
6
7
1
5
9
2
3
4
8
6
7
1
5
9
Notes: We can now address the questions raised by our second motivating example. By Theorem 3, we find that each of these graphs is strong graph structurally controllable with either node 6 or node 8 as the leader. Here, let us consider node 6 to be the leader in the upper system. We can now consider the lower system with node 6 as the leader to begin with. We can then connect the last node in the Hamiltonian path of the upper graph, i.e., node 4 to node 6 of the lower graph and at the same time make node 6 a follower, then the coupled system is controllable. We could have also considered node 8 to be the leader in the lower graph and then the connection would have to be from node 4 of the upper graph to node 8 of the lower graph to make the cascaded system controllable.

## Slide 17: Proof sketch – Theorem: 3
Step 1: Matrix A^k has an almost lower triangular structure
Step 2: Controllability matrix C is upper triangular
Notes: Due to time constraints, I shall briefly sketch the proofs of the theorems for sufficient conditions for strong graph structural controllability and the theorem with a necessary condition for string graph structural controllability. I start with the sufficiency theorem. The first step in proving this theorem involves the structure of the matrices formed by the various powers of matrix A. Since we know that A is an in-Laplacian and we have a Hamiltonian path in the graph with no forward edges, we have that A is almost lower triangular, i.e., it is lower triangular with an added non-zero superdiagonal. Using an induction argument, we can show that this structure holds for all powers of A as well. Using this result, we can show that the controllability matrix C of this system is upper triangular with diagonal terms given here. Since all these diagonal terms are non-zero, C is full rank. Since C is upper-triangular, we can get its determinant as the product of its diagonal terms. Further we can get the eigenvalues of C as the roots of the determinant of lambda I – C, which is also an upper triangular matrix, thus yielding our final result.

## Slide 18: Proof sketch – Theorem: 4
Step 1: Construct a left-eigenvector of A
Step 2: Note that this is also a null vector of B
By PBH test, we show that system is not controllable
Notes: We can break this proof down into two key steps. We first construct a vector v as shown here, which we prove is a left eigenvector of A. In the second step, we note that this vector is also a null-vector of B when the weights satisfy the condition stated here. Then by the PBH test, we have that the system is not controllable.

## Slide 19: Conclusion
Identified the concepts of graph structural controllability and strong graph structural controllability in linear leader-follower systems on directed graphs.
Proved:
  Accessibility from a leader is a necessary and sufficient condition for graph structural controllability.
  Existence of a Hamiltonian path and absence of other forward-pointing edges (with respect to the Hamiltonian path) is sufficient for strong graph structural controllability.
  A necessary condition for loss of strong graph structural controllability, involving a triangle subgraph.
  Role played by strong graph structural controllability in preserving controllability when two dynamical systems are cascaded.
Future work: Necessary condition for strong graph structural controllability
Notes: I will now summarize the key points of this talk. We have identified the concepts of graph structural controllability and string graph structural controllability in linear leader-follower systems on directed graphs. We have highlighted the distinction between these concepts and the concepts of structural controllability and string structural controllability already present in literature and also justified the necessity of these for leader-follower systems. We have proved 4 key results: accessibility is a necessary and sufficient condition for graph structural controllability. Existence of a Hamiltonian path with no additional forward pointing edges is a sufficient condition for string graph structural controllability. Presence of a particular triangle sub-graph results in loss of strong graph structural controllability and finally a result on controllability of cascades. We are still working on deriving a necessary condition for strong graph structural controllability. If someone in the audience has any ideas, we will be happy to discuss. Thanks.

## Slide 20
Thank you